## Slide 1: SHETran Results Viewer
Guidance for users

## Slide 2
Run the program SHETran-Results-Viewer-*.*.*.exe
Select library file (.xml) from model folder
Enter model name (or accept default)

## Slide 3
Select variable
Drop-down list of variables available for this model run
Note: different variables can be defined during model setup

## Slide 4
Add model
Results from multiple models can be shown for comparison

## Slide 5
Model list
List of available models, showing full folder path

## Slide 6
Rename model
Renames the selected model

## Slide 7
Remove model
Remove model from list (only works if multiple models present)

## Slide 8
Map display
Shows selected variable for selected model run

## Slide 9
Map display
Some variables are set up only for the river network
For example, to show the catchment discharge hydrograph, select
Overland Flow (m3/s) variable
River outlet link

## Slide 10
Reset view
Centres the model view

## Slide 11
Graph plot
Shows time-series graph for selected grid element for one or more model runs
Title shows:
Element number
Ground elevation
X,Y real world co-ordinates

## Slide 12
Click/hover
Radio button to allow click or hover cursor over map grid elements, to select data for graph display

## Slide 13
Difference
Check box to show difference between two model runs
Plot shows difference between first model and another model selected from the drop-down list

## Slide 14
Time slider bar
Click and drag to animate the map view

## Slide 15
Zoom slider bar
Click and drag to zoom the graph display around the selected time

## Slide 16
Add series
Add a time-series from a .csv file with one date column and one data column (any additional data columns will be ignored)
Can be used for comparison with observed data
Note: the data will be shown on the graph until the ‘Clear Series’ button is pressed or difference mode activated

## Slide 17
Download
Download the visible graph time-series data to a .csv file

## Slide 18
Monthly Means
Option to resample values into a monthly time series

## Slide 19
NSE
Nash Sutcliffe Efficiency is shown in brackets when an observed series is present